## Slide 1: Hur många mikroprocessorer ser vi på bilden?
mikroprocessor, definition:
A microprocessor is an integrated circuit that contains a central processing unit, executing instructions to perform arithmetic, logic, control, and input–output operations.
Notes: Welcome to this course in Machine Oriented Programming! In a previous course, you have seen how simple logic gates can be combined to create an ALU, a data path, and finally a complete working tiny processor. In this course you will build on this knowledge and learn how to program a real, modern, off-the-shelf microcontroller 1. You will develop programs for this device using assembly and C and you will learn how to communicate with peripheral devices (lights, buttons, displays and a tiny speaker).

## Slide 2: Maskinorienterad Programmering
Lektion 1 - Introduktion
Notes: Welcome to this course in Machine Oriented Programming!

## Slide 3: Maskinorienterad Programmering
Notes: In a previous course, you have seen how simple logic gates can be combined to create an ALU, a data path, and finally a complete working tiny processor. In this course you will build on this knowledge and learn how to program a real, modern, off-the-shelf microcontroller 1. You will develop programs for this device using assembly and C and you will learn how to communicate with peripheral devices (lights, buttons, displays and a tiny speaker).
As illustrated in the image below, the course is also a prerequisite for several upcoming courses.

## Slide 4
Laptop ~50 mikroprocessorer
A modern laptop typically contains dozens of microprocessors (often between 30 and 100), most of which are microcontrollers (MCUs) embedded in subsystems such as power management, battery control, keyboard and touchpad controllers, storage devices, display interfaces, networking hardware, cameras, and security modules.
Telefon ~30 mikroprocessorer power management, battery charging, touch sensing, cameras, audio, wifi, ...
Bluetoothlurar ~10? power management, battery charging, audio, Bluetooth, ...
Frys/Kyl, 20? temperature control, inverter drive, frost cycles, valve actuation, ...
Brödrost!? Åtminstone en (timing)
USB Laddare: 1-3? manage voltage regulation, current limiting, thermal protection, and fault handling.
Min bil? ~100?
allt möjligt
Notes: Welcome to this course in Machine Oriented Programming! In a previous course, you have seen how simple logic gates can be combined to create an ALU, a data path, and finally a complete working tiny processor. In this course you will build on this knowledge and learn how to program a real, modern, off-the-shelf microcontroller 1. You will develop programs for this device using assembly and C and you will learn how to communicate with peripheral devices (lights, buttons, displays and a tiny speaker).
JOBS!

## Slide 5: ”The Maker Community”
Efter den här kursen kommer ni kunna programmera en mikrokontroller
Internet är proppfullt av roliga projekt som folk gör med sina mikrokontrollers:
  https://www.seeedstudio.com/blog/2021/03/26/10-raspberry-pi-pico-projects/
  https://projecthub.arduino.cc/
  https://www.allaboutcircuits.com/projects/category/embedded/microcontroller/
  ...

## Slide 6: Vad är en mikrokontroller?